## Slide 1: Caches and Memory Hierarchy: Review
UCSB CS240A, Fall 2017

## Slide 2: Motivation
Most applications in a single processor runs at only 10-20% of the processor peak
Most of the single processor performance loss is in the memory system
  Moving data takes much longer than arithmetic and logic
Parallel computing with low single machine performance is not good enough.
  Understand high performance computing and cost in a single machine setting
Review of cache/memory hierarchy

## Slide 3: Typical Memory Hierarchy
Second-Level
Cache
(SRAM)
Control
Datapath
Secondary
Memory
(Disk
Or Flash)
On-Chip Components
RegFile
Main
Memory
(DRAM)
Data
Cache
Instr
Cache
Speed (cycles): ½’s 1’s 10’s 100’s 1,000,000’s
Size (bytes): 100’s 10K’s M’s G’s T’s
Principle of locality + memory hierarchy presents programmer with ≈ as much memory as is available in the cheapest technology at the ≈ speed offered by the fastest technology
Cost/bit: highest lowest
Third-Level
Cache
(SRAM)
Notes: Instead, the memory system of a modern computer consists of a series of black boxes ranging from the fastest to the slowest.
Besides variation in speed, these boxes also varies in size (smallest to biggest) and cost.
What makes this kind of arrangement work is one of the most important principle in computer design. The principle of locality. The principle of locality states that programs access a relatively small portion of the address space at any instant of time.
The design goal is to present the user with as much memory as is available in the cheapest technology (points to the disk).
While by taking advantage of the principle of locality, we like to provide the user an average access speed that is very close to the speed that is offered by the fastest technology.
(We will go over this slide in detail in the next lectures on caches).

## Slide 4: Idealized Uniprocessor Model
Processor names bytes, words, etc. in its address space
  These represent integers, floats, pointers, arrays, etc.
Operations include
  Read and write into very fast memory called registers
  Arithmetic and other logical operations on registers
Order specified by program
  Read returns the most recently written data
  Compiler and architecture translate high level expressions into “obvious” lower level instructions
  Hardware executes instructions in order specified by compiler
Idealized Cost
  Each operation has roughly the same cost
    (read, write, add, multiply, etc.)
A = B + C 
Read address(B) to R1
Read address(C) to R2
R3 = R1 + R2
Write R3 to Address(A)

## Slide 5: Uniprocessors in the Real World
Real processors have
  registers and caches
    small amounts of fast memory
    store values of recently used or nearby data
    different memory ops can have very different costs
  parallelism
    multiple “functional units” that can run in parallel
    different orders, instruction mixes have different costs
  pipelining
    a form of parallelism, like an assembly line in a factory
Why is this your problem?
    In theory, compilers and hardware “understand” all this and can optimize your program; in practice they don’t.
    They won’t know about a different algorithm that might be a much better “match” to the processor

## Slide 6: Memory Hierarchy
Most programs have a high degree of locality in their accesses
  spatial locality: accessing things nearby previous accesses
  temporal locality: reusing an item that was previously accessed
Memory hierarchy tries to exploit locality to improve average
on-chip cache
registers
datapath
control
processor
Second level cache (SRAM)
Main memory
(DRAM)
Secondary storage (Disk)
Tertiary storage
(Disk/Tape)
Speed | 1ns | 10ns | 100ns | 1-10ms | 10sec
Size | KB | MB | GB | TB | PB

## Slide 7: Review: Cache in Modern Computer Architecture
Processor
Control
Datapath
PC
Registers
Arithmetic & Logic Unit
(ALU)
Memory
Input
Output
Bytes
Address
Write Data
ReadData
Processor-Memory Interface
I/O-Memory Interfaces
Program
Data
Cache

## Slide 8: Cache Basics
Cache is fast (expensive) memory which keeps copy of data in main memory; it is hidden from software
  Simplest example: data at memory address xxxxx1101 is stored at cache location 1101
Memory data is divided into blocks
  Cache access memory by a block (cache line)
  Cache line length: # of bytes loaded together in one entry
Cache is divided by the number of sets
  A cache block can be hosted in one set.
Cache hit: in-cache memory access—cheap
Cache miss: Need to access next, slower level of cache

## Slide 9: Memory Block-addressing example

## Slide 10: Processor Address Fields used by Cache Controller
Block Offset: Byte address within block
  B is number of bytes per block
Set Index: Selects which set. S is the number of sets
Tag: Remaining portion of processor address
Size of Tag = Address size – log(S) – log(B)
Block offset
Set Index
Tag
Processor Address
Cache Size C = Associativity N × # of Set S × Cache Block Size B
Example: Cache size 16K. 8 bytes as a block.  2K blocks  If N=1, S=2K using 11 bits.
Associativity N represents # items that can be held per set
Notes: For class handout

## Slide 11: Block number aliasing example
Block #
Block # mod 8
Block # mod 2
12-bit memory addresses, 16 Byte blocks
3-bit set index
1-bit set index

## Slide 12: Direct-Mapped Cache: N=1. S=Number of Blocks=210
4byte blocks, cache size = 1K words (or 4KB)
20
Tag
10
Index
Data
Index
Tag
Valid
0
1
2
.
.
.
1021
1022
1023
31 30 . . . 13 12 11 . . . 2 1 0
Byte offset
20
Data
32
Hit
Valid bit ensures something useful in cache for this index
Compare Tag with upper part of Address to see if a Hit
Read data from cache instead of memory if a Hit
Comparator
Cache Size C = Associativity N × # of Set S × Cache Block Size B
Notes: Let’s use a specific example with realistic numbers: assume we have a 1 K word (4Kbyte) direct mapped cache with block size equals to 4 bytes (1 word).
In other words, each block associated with the cache tag will have 4 bytes in it (Row 1).
With Block Size equals to 4 bytes, the 2 least significant bits of the address will be used as byte select within the cache block.
Since the cache size is 1K word, the upper 32 minus 10+2 bits, or 20 bits of the address will be stored as cache tag.
The rest of the (10) address bits in the middle, that is bit 2 through 11, will be used as Cache Index to select the proper cache entry
Temporal!

## Slide 13: Cache Organizations
“Fully Associative”: Block can go anywhere
  N= number of blocks. S=1
“Direct Mapped”: Block goes one place
  N=1. S= cache capacity in terms of number of blocks
“N-way Set Associative”: N places for a block
Block ID
Block ID
13
Cache Size C = N × # of Set S × Size B
Associativity N represents # items that can be held per set

## Slide 14: Four-Way Set-Associative Cache
28 = 256 sets each with four ways (each with one block)
31 30 . . . 13 12 11 . . . 2 1 0
Byte offset
Data
Tag
V
0
1
2
.
.
.
253
254
255
Data
Tag
V
0
1
2
.
.
.
253
254
255
Data
Tag
V
0
1
2
.
.
.
253
254
255
Set Index
Data
Tag
V
0
1
2
.
.
.
253
254
255
8
Index
22
Tag
Hit
Data
32
4x1 select
Way 0
Way 1
Way 2
Way 3
Notes: This is called a 4-way set associative cache because there are four cache entries for each cache index. Essentially, you have four direct mapped cache working in parallel.
This is how it works: the cache index selects a set from the cache. The four tags in the set are compared in parallel with the upper bits of the memory address.
If no tags match the incoming address tag, we have a cache miss.
Otherwise, we have a cache hit and we will select the data from the way where the tag matches occur.
This is simple enough. What is its disadvantages?
+1 = 36 min. (Y:16)

## Slide 15: How to find if a data address in cache?
Assume block size 8 bytes last 3 bits of address are offset.
Set index 2 bits.
Given address 0b1001011, where to find this item from cache?
0b means binary number

## Slide 16: How to find if a data address in cache?
Assume block size 8 bytes last 3 bits of address are offset.
Set index 2 bits.
0b1001011  Block number 0b1001.
Set index 2 bits (mod 4)
  Set number  0b01.
Tag = 0b10.
  If directory based cache, only one block in set #1.
  If 4 ways, there could be 4 blocks in set #1.
  Use tag 0b10 to compare what is in the set.
0b means binary number

## Slide 17: Cache Replacement Policies
Random Replacement
  Hardware randomly selects a cache evict
Least-Recently Used
  Hardware keeps track of access history
  Replace the entry that has not been used for the longest time
  For 2-way set-associative cache, need one bit for LRU replacement
Example of a Simple “Pseudo” LRU Implementation
  Assume 64 Fully Associative entries
  Hardware replacement pointer points to one cache entry
  Whenever access is made to the entry the pointer points to:
    Move the pointer to the next entry
  Otherwise: do not move the pointer
  (example of “not-most-recently used” replacement policy)
:
Entry 0
Entry 1
Entry 63
Replacement
Pointer

## Slide 18: Handling Data Writing
Store instructions write to memory, changing values
Need to make sure cache and memory have same values on writes: 2 policies
  1) Write-through policy: write cache and write through the cache to memory
    Every write eventually gets to memory
    Too slow, so include Write Buffer to allow processor to continue once data in Buffer
    Buffer updates memory in parallel to processor
  2) Write-back policy

## Slide 19: Write-Through Cache
Write both values in cache and in memory
Write buffer stops CPU from stalling if memory cannot keep up
Write buffer may have multiple entries to absorb bursts of writes
What if store misses in cache?
Processor
32-bit
Address
32-bit
Data
Cache
32-bit
Address
32-bit
Data
Memory
1022
99
252
7
20
12
131
2041
Addr
Data
Write Buffer

## Slide 20: Handling Stores with Write-Back
2) Write-Back Policy: write only to cache and then write cache block back to memory when evict block from cache
  Writes collected in cache, only single write to memory per block
  Include bit to see if wrote to block or not, and then only write back if bit is set
    Called “Dirty” bit (writing makes it “dirty”)

## Slide 21: Write-Back Cache
Store/cache hit, write data in cache only & set dirty bit
  Memory has stale value
Store/cache miss, read data from memory, then update and set dirty bit
  “Write-allocate” policy
Load/cache hit, use value from cache
On any miss, write back evicted block, only if dirty. Update cache with new block and clear dirty bit.
Processor
32-bit
Address
32-bit
Data
Cache
32-bit
Address
32-bit
Data
Memory
1022
99
252
7
20
12
131
2041
D
D
D
D
Dirty Bits

## Slide 22: Write-Through vs. Write-Back
Write-Through:
  Simpler control logic
  More predictable timing simplifies processor control logic
  Easier to make reliable, since memory always has copy of data (big idea: Redundancy!)
Write-Back
  More complex control logic
  More variable timing (0,1,2 memory accesses per cache access)
  Usually reduces write traffic
  Harder to make reliable, sometimes cache has only copy of data

## Slide 23: Cache (Performance) Terms
Hit rate: fraction of accesses that hit in the cache
Miss rate: 1 – Hit rate
Miss penalty: time to replace a block from lower level in memory hierarchy to cache
Hit time: time to access cache memory (including tag comparison)

## Slide 24: Average Memory Access Time (AMAT)
Average Memory Access Time (AMAT) is the average time to access memory considering both hits and misses in the cache
  AMAT = Time for a hit + Miss rate × Miss penalty
Given a 0.2ns clock, a miss penalty of 50 clock cycles, a miss rate of 2% per instruction and a cache hit time of 1 clock cycle, what is AMAT?
AMAT = 1 cycle + 0.02*50 = 2 cycles = 0.4ns.
Notes: AMAT = 1 + 0.02x50 = 2